## Slide 1
AI-Based Ground Vibration Detection
Human / Vehicle Activity Classification
An integrated AECD + Signal Processing + Machine Learning safety-monitoring prototype
AECD
Capture & condition the weak
vibration signal
SIGNAL PROCESSING
Clean, analyze & extract features
ML
Classify activity & generate an alert

## Slide 2
1. Problem & Proposed Solution
Detect meaningful ground vibration and identify the activity behind it.
Ground vibrations can indicate nearby activity when optical monitoring is difficult.
Camera-based systems can be limited by darkness, fog, dust, foliage or line-of-sight.
Our system senses vibration, processes it and uses ML to classify the activity.
Prototype classes: No activity, Human footsteps, Light vehicle, Other vibration.
INPUT
Mechanical vibration in the ground
CORE PIPELINE
AECD → SP → ML
OUTPUT
Activity class + alert

## Slide 3
2. How AECD, SP and ML are interlinked
GROUND
Piezo / vibration sensor
AECD
Amplifier + active filter + buffer
SP
Sampling + digital filter + FFT + RMS
ML
Features → classifier
ALERT
OLED / LED / buzzer
KEY IDEA
The output of one subject becomes the input to the next: Electronics → Signal → Features → Intelligence.

## Slide 4
3. AECD: Making the weak sensor signal usable
Piezoelectric vibration sensor converts mechanical vibration into a small electrical signal.
LM358 / suitable op-amp provides amplification and buffering.
An active band-pass / low-pass stage removes unwanted frequency content.
Anti-aliasing filtering prepares the signal before ADC sampling.
Decoupling and clean grounding improve measurement reliability.
SENSOR
Piezo vibration transducer
AMPLIFIER
LM358 / TL072
FILTER
Active band-pass / LPF
OUTPUT
Conditioned analog signal

## Slide 5
4. Signal Processing: From vibration to features
Sample the conditioned signal using the microcontroller ADC.
Use digital FIR/IIR filtering to suppress unwanted noise.
FFT shows the frequency content of the vibration.
RMS measures signal energy and helps distinguish weak and strong events.
Extract features such as RMS, dominant frequency, peak amplitude and band energy.
TIME DOMAIN
Waveform + RMS
FREQUENCY DOMAIN
FFT + dominant frequency
FEATURE VECTOR
Numbers supplied to ML
RESULT
Clean, informative data

## Slide 6
5. Machine Learning: Classifying the activity
Collect labelled vibration recordings for each activity class.
Convert each recording window into a feature vector from the SP stage.
Train a lightweight Decision Tree or Random Forest classifier.
Evaluate with accuracy, precision, recall, F1-score and a confusion matrix.
If feasible, deploy the lightweight model for real-time embedded inference.
INPUT FEATURES
RMS | FFT | Peaks | Band energy
MODEL
Decision Tree / Random Forest
CLASSES
Human | Vehicle | Other | None
OUTPUT
Class + alert

## Slide 7
6. Real-World Significance
Potential civilian and industrial applications
INFRASTRUCTURE
Monitor restricted areas,
construction zones and isolated facilities
for unusual activity.
INDUSTRIAL SAFETY
Detect abnormal vibration around
machinery, access zones or facilities.
SMART-CITY MONITORING
Complement cameras and other sensors
with low-power ground sensing.
LOW LINE-OF-SIGHT DEPENDENCE
Ground vibration can complement
optical monitoring when visibility is poor.
EDGE INTELLIGENCE
Local processing can reduce the need to
stream raw sensor data.
SCALABLE
Multiple sensor nodes could feed a
central dashboard in future work.

## Slide 8
7. Components & Models
SENSOR
Piezoelectric vibration transducer
ANALOG FRONT END
LM358/TL072 + R/C network + active filters
CONTROLLER
ESP32 or STM32 with ADC
OUTPUT
OLED + LED/buzzer alert
DSP
Python/NumPy/SciPy during development;
embedded DSP for final prototype
ML
Scikit-learn Decision Tree / Random Forest
DATASET
Self-collected, labelled vibration data
DEMO
Real-time activity detection + alert

## Slide 9
9. Why this is a strong integrated project
AECD
We physically acquire and condition a
weak sensor signal using amplifiers,
active filters, buffers, power and
grounding.
SIGNAL PROCESSING
We sample, filter and analyze the
vibration in time/frequency domains,
then create meaningful features.
MACHINE LEARNING
We learn the relationship between
vibration features and activity classes,
then classify new events.
ONE CONTINUOUS PIPELINE
Physical world → Electronics → Signal → Features → Intelligence → Safety decision