## Slide 1
PROJECT // GROUND VIBRATION DETECTION
Ground Vibration
Detection
A complete sensor-to-alert workflow that turns weak ground motion into live, intelligent classification using AI-based signal processing.
01
PIEZO
SENSOR
02
ANALOG
FRONT END
03
SIGNAL
PROCESSING
04
ML
CLASSIFIER
05
SMART
ALERT

## Slide 2
SIGNAL PATH
mV SPIKE
↓ Amp · LPF
0–3.3 V
↓ ADC · 8 kHz
FFT / RMS
↓ Random Forest
CLASS ID
SYSTEM ARCHITECTURE // OVERVIEW
One signal, five transformations
PIEZO SENSOR
Converts mechanical ground vibration into millivolt-level electrical signals.
ANALOG FRONT END
Amplification, biasing, and low-pass filtering (100Hz cutoff).
SIGNAL PROCESSING
ADC sampling, software filtering, and feature extraction (FFT/RMS).
ML CLASSIFIER
Random Forest model predicts activity class from extracted features.
SMART ALERT
Visual (OLED) and audible/visual (Buzzer/LED) feedback.
ANALOG DOMAIN
DIGITAL DOMAIN

## Slide 3
SUBJECT 1 // ANALOG CONDITIONING
AECD: Make the signal usable
01
PIEZO
02
AMP
(G=21)
03
LPF
(100Hz)
04
BUFFER
OP-AMP | LM358 Dual
BIASING | 4.5V Virtual GND
LPF CUTOFF | 100 Hz
SUPPLY | 9V DC
DESIGN OBJECTIVES
Amplification: Raises millivolt-level piezo spikes to a usable 0-3.3V range for the ESP32 ADC.
Single-Supply Biasing: Creates a stable virtual ground at Vcc/2, allowing the AC vibration signal to swing without clipping.
Hardware Filtering: RC low-pass filter removes high-frequency electrical noise and irrelevant vibrations above 100Hz.
Impedance Matching: Final buffer stage ensures the signal isn't loaded down by the ADC input.

## Slide 4
SUBJECT 2 // DIGITAL SIGNAL PROCESSING
Signal processing: Expose the pattern
SAMPLE WINDOW
2 s
16,000 samples @ 8000 Hz
1. SAMPLING
ESP32 ADC captures the signal at 8000 Hz. Data is buffered into 2-second windows (16,000 samples) for analysis.
2. SOFTWARE FILTER
A 4th-order Butterworth Low-Pass Filter (100Hz cutoff) is applied in software to further isolate the ground vibration signatures.
3. FEATURE EXTRACTION
The raw window is compressed into four key mathematical features that define the vibration "fingerprint":
RMS
Energy Level
PEAK
Max Amplitude
DOMINANT FREQ
Spectral Peak
BAND ENERGY
1-50Hz Power

## Slide 5
SUBJECT 3 // DATA COLLECTION
Data collection: Teach the system context
PROTOCOL
Fixed Placement: Sensor taped to a consistent surface to maintain gain integrity.
Class Diversity: 20-30 samples per class (No activity, Footsteps, Vehicle, Other).
Immediate Labeling: Filenames indexed by class (e.g., footsteps_001.wav) to prevent drift.
Windowing: Each sample is a discrete 2-second capture.
RMS | PEAK | DOM FREQ | LABEL
0.0042 | 0.012 | 12.5 Hz | No Activity
0.0850 | 0.420 | 24.0 Hz | Footsteps
0.1420 | 0.680 | 48.5 Hz | Vehicle
0.0560 | 0.210 | 110.0 Hz | Other
Target: 100+ rows in dataset.csv
Structured samples connect each 2-second capture to a known class and a measurable fingerprint.

## Slide 6
SUBJECT 4 // MACHINE LEARNING
Machine learning: Classify the event
FEATURE VECTOR
RMS · PEAK · FREQ · BAND
Random Forest
50 Trees
Max Depth
5 Levels
Test Split
25%
Success Rate
90%+
The model acts as a multi-class decision engine, mapping the 4D feature vector to one of four classes:
0: No Activity
Low RMS, low peak, white noise spectrum.
1: Human Footsteps
Rhythmic RMS spikes, low frequency (10-30Hz).
2: Light Vehicle
Sustained high RMS, mid frequency (30-60Hz).
3: Other Vibration
High peak, erratic frequency distribution.
Feature Importance
RMS Energy
Feature Importance
Dominant Frequency

## Slide 7
INTERFACE MAP
ESP32 ⇄ LAPTOP
Serial · raw ADC ↔ class ID
OUTPUTS
OLED · BUZZER · LED
GPIO logic-level triggers
SUBJECT 5 // SYSTEM INTEGRATION
Embedded integration: Close the loop
01
LAPTOP-SERIAL APPROACH (RECOMMENDED)
ESP32 streams raw ADC values over Serial. A Python script on the laptop handles windowing, feature extraction, and ML inference. This allows for rapid debugging and visualization.
02
BI-DIRECTIONAL FEEDBACK
The laptop sends the predicted class ID back to the ESP32. The ESP32 then triggers the local hardware (OLED/Buzzer) based on the received command.
03
FULLY EMBEDDED (STRETCH GOAL)
Convert the Random Forest decision rules into C++ if/else logic. Run the entire pipeline—sampling to classification—locally on the ESP32 for a standalone product.

## Slide 8
SUBJECT 6 // ALERT SYSTEM
Alert layer: Turn prediction into action
CLASS | ALERT MAPPING
FOOTSTEPS | OLED: "HUMAN DETECTED" + LED BLINK
VEHICLE | OLED: "VEHICLE ALERT" + BUZZER ON
OTHER | OLED: "UNKNOWN VIBE"
Nfrom where didi you geONE | OLED: "SYSTEM READY"
OLED Display
I2C SSD1306 0.96" shows real-time class name.
Active Buzzer
Audible alert for high-priority (vehicle) events.
LED Indicator
Visual pulse for human footstep detection.
ESP32 GPIO
Logic-level triggers for all peripheral outputs.

## Slide 9
VALIDATION // QUALITY CONTROL
Integration is a sequence of go/no-go checks
SUCCESS CRITERIA
Analog Check: Tapping the piezo produces a visible voltage swing on the multimeter/oscilloscope.
DSP Check: Filtered software signal shows clear pulse separation compared to raw ADC noise.
ML Check: Confusion matrix shows minimal overlap between "Footsteps" and "Vehicle" classes.
GO / NO-GO GATES
3 / 3
COMMON FAILURE POINTS
Floating Ground: Biasing network failure leads to signal clipping at the 0V rail.
Overfitting: Collecting data only in one room leads to failure when moved to a different floor type.
Latency: 2-second windows are too long for real-time alerts; consider overlapping windows.

## Slide 10
PROJECT // CONCLUSION
A complete engineering story
From the first millivolt spike to a smart OLED alert, this prototype demonstrates the power of integrating analog design with modern machine learning.
SCALING
Deploy a mesh of sensors to triangulate the exact location of the vibration source.
OPTIMIZATION
Prune the Random Forest for ultra-low power consumption on battery-operated nodes.
EXPANSION
Add "Seismic Event" and "Industrial Machinery" classes for broader use cases.