## Slide 1
REVIEW 3 | METHODOLOGY DEVELOPMENT
AI-Based Ground Vibration Detection
Human / Vehicle Activity Classification
A low-cost sensing pipeline combining analog electronics, digital signal processing and machine learning.
TEAM MEMBERS
G. Akshith • K. Ahladh • P. Cyril Raj K. Sravya • B. Gowri
Guides: A. Bhuvaneshwari (AECD) | Ashwini Kumar Varma (Signal Processing) Gangamohan Paidi (Machine Learning)

## Slide 2
Problem, Research Gap & Objectives
Why ground vibration can complement visibility-based monitoring
02 / 07
THE PROBLEM
• Cameras can struggle in darkness, fog, dust, foliage and obstructed views.
• Footsteps, vehicles and other events create different ground-vibration patterns.
THE GAP
• A low-cost, integrated pipeline is needed to sense, process and classify vibration.
• Real-world performance still needs validation using labelled hardware recordings.
PROJECT OBJECTIVES
• Condition and digitise the weak piezo signal.
• Extract signal features and compare Decision Tree vs Random Forest.
• Display class and raise a local alert.
FOUR TARGET CLASSES
01
No activity
02
Human footsteps
03
Light vehicle
04
Other vibration
Core aim: detect activity independently of visibility and classify the source from its vibration signature.

## Slide 3
Proposed Methodology
End-to-end workflow: sense → condition → analyse → classify → alert
03 / 07
1
SENSE
Piezoelectric transducer
2
CONDITION
Amplify, bias and analog LPF
3
DIGITISE
ESP32 ADC at 2 kHz
4
FILTER
101-tap FIR 5–400 Hz
5
EXTRACT
1 s windows + 6 features
6
CLASSIFY
Decision Tree / Random Forest
7
ALERT
OLED + LED / buzzer
FEATURE VECTOR PER 1-SECOND WINDOW
RMS • Peak amplitude • Dominant FFT frequency • Energy: 5–50 Hz • 50–150 Hz • 150–400 Hz
Alert rule: show the predicted class; activate an LED for activity and buzzer for footsteps / light vehicle. Two consecutive matching windows may reduce false alarms.

## Slide 4
System Architecture & Design
Three course stages integrated into one sensor node
04 / 07
AECD • ANALOG FRONT END
• Piezo sensor + 1 MΩ load
• Spike protection: 1N4148
• AC coupling + 1.65 V bias
• Non-inverting gain ≈ 22
• Sallen-Key LPF ≈ 408 Hz + buffer
SIGNAL PROCESSING
• ESP32 ADC: 2 kHz, 12-bit
• 1-second window (2000 samples)
• Hamming FIR band-pass: 5–400 Hz
• Hanning window + FFT / RMS
• Six-element feature vector
MACHINE LEARNING
• Labelled windows: 4 classes
• Decision Tree: depth 4
• Random Forest: 100 trees
• Evaluate accuracy, precision,
• recall, F1-score + confusion matrix
OUTPUT LAYER
OLED class display • LED activity indicator • Buzzer alert
Controller / target: ESP32 or STM32 with ADC; lightweight on-device inference is a planned extension.

## Slide 5
Tools, Technologies & Key Parameters
Design choices currently specified in the project report
05 / 07
HARDWARE
• Piezoelectric vibration transducer
• LM358 or TL072 op-amp
• ESP32 / STM32 microcontroller
• OLED, LED and buzzer
SOFTWARE
• Python, NumPy and SciPy
• scikit-learn classifiers
• Multisim circuit simulation
• Wokwi / breadboard test setup
SIGNAL / ML SETTINGS
• Sampling rate: 2,000 Hz
• FIR: 101 taps, Hamming window
• Band-pass: 5–400 Hz
• Decision Tree depth 4; RF 100 trees
IMPORTANT ANALOG DESIGN VALUES
Bias
1.65 V
Amplifier gain
≈ 22
Analog low-pass
≈ 408 Hz
AC-coupling corner
≈ 3.2 Hz
Window length
1 second / 2,000 samples
The analog front end is specified by design calculations; its bench verification remains part of the next phase.

## Slide 6
Work Completed & Preliminary Results
Signal-processing and ML pipeline tested on synthetic data
06 / 07
CURRENT IMPLEMENTED WORK
• 960 synthetic one-second windows
• 240 windows per class
• 720 training / 240 test windows
• FIR filtering and six-feature extraction
• Decision Tree and Random Forest trained
• Five-fold cross-validation completed
Important limitation: results are from synthetic data, not real field recordings.
TEST ACCURACY (240-WINDOW TEST SET)
Decision Tree
67.5%
Random Forest
75.4%
5-FOLD CROSS-VALIDATION
Decision Tree 0.809 ± 0.052
Random Forest 0.864 ± 0.065
Interpretation: Random Forest performed better in the current synthetic-data evaluation. Field accuracy is not yet established.

## Slide 7
Validation Plan & Next Steps
Priorities leading to Review 4: validate the physical prototype
07 / 07
01
Verify circuit
Simulate in Multisim; build breadboard front end; check 5 V rail, 1.65 V bias and gain ≈ 22.
02
Capture real signals
Connect sensor to controller; sample at 2 kHz; inspect waveforms and ADC range.
03
Build labelled dataset
Record quiet, footsteps, light vehicle and other vibration at different distances / surfaces.
04
Retrain + evaluate
Compare classifiers on real data; report accuracy, precision, recall, F1 and confusion matrix.
05
Integrate live alert
Show class on OLED; activate LED / buzzer; explore ESP32 inference.
SUCCESS CHECKS: stable analog output • no ADC saturation • 2 kHz sampling ±1% • ≥100 real windows per class • correct live class / alert